## Slide 1: Heartbeat classification with ANN (MIT-BIH dataset)
Zhanna Hakhverdyan
04.30.20

## Slide 2: Problem statement
Arrhythmia diagnosis requires many hours worth of ECG signal interpretation
Manual analysis is time and labor intensive
The ECG test administrations are expected to grow
There is a need for reliable automated tools for beat classification

## Slide 3: Dataset description
MIT-BIH arrhythmia dataset:
https://physionet.org/content/mitdb/1.0.0/
48 30 min ECG recordings from 47 subjects
2-lead ECG signal
109,000 beat labels

## Slide 4: 5 standard heartbeat classes*
* Specified in ANSI/AAMI EC57:1998/(R)2008
1.
2.
3.
4.
5.

## Slide 5: Arrhythmic beats are an unevenly distributed minority
Class | Count | Fraction
N | 90125 | 0.895
S (SVEB) | 2781 | 0.028
V (VEB) | 7009 | 0.070
F | 803 | 0.008
Q | 15 | 0.000 (class excluded, too few)

## Slide 6: Heartbeat morphology variation
Average +/- 1 standard deviation, record # 114
N S V F
Peak inversion
Baseline drift
a. Non-biological, intra-record variation
b. Biological, inter-record variation
Average +/- 1 standard deviation, record # 222
N S
Different patient
Canonical heartbeat

## Slide 7: Feature transformation steps
Variation source | Transformation / action
Baseline drift | Take the difference of consecutive points
Peak inversion | Take the absolute value of the signal
Different patients | Split the dataset for training on patient records
Average +/- 1 standard deviation AFTER
N S V F
Average +/- 1 standard deviation BEFORE
N S V F

## Slide 8: Split Train, Val, Test sets on records
Dataset | # of records | N count (%) | S count (%) | V count (%) | F count (%)
Train | 30 | 59446 (88.8) | 2330 (3.5) | 4768 (7.1) | 403 (0.6)
Validation | 4 | 9015 (91.4) | 140 (1.4) | 685 (6.9) | 20 (0.2)
Test | 10 | 21664 (90.6) | 311 (1.3) | 1556 (6.5) | 380 (1.6)
Total | 44 | 90125 (89.5) | 2781 (2.8) | 7009 (7.0) | 803 (0.8)
Dataset composition (record #)
Train: 101, 103, 105, 106, 109, 111, 112, 113, 115, 116, 117, 119, 121, 122, 123, 200, 201, 202, 205, 207, 208, 209, 212, 219, 221, 222, 230, 231, 232, 233
Validation: 100, 124, 215, 223
Test: 108, 114, 118, 203, 210, 213, 214, 220, 228, 234

## Slide 9: 2-dimensional visualization with PCA
PCA of transformed dataset
The 4 classes are not well separated

## Slide 10: Dimensionality reduction: PCA
The first 5 PCs account for the most variance
The first 20 PCs represent ~80% of variance
Next: apply machine learning models on PCA-transformed dataset (20 PCs)

## Slide 11: Ensemble models have poor precision and sensitivity
Example learning curves for random forest tuning
 | V class |  |  |  | S class |  |  |  | F class | All classes | 
Model/metric* | Se | Pr | FPR | Acc | Se | Pr | FPR | Acc | Se | Sp | Acc
RF | 0.531 | 0.604 | 0.024 | 0.947 | 0.003 | 0.05 | 0.001 | 0.986 | 0 | 0.928 | 0.876
GBC | 0.584 | 0.38 | 0.067 | 0.911 | 0.026 | 0.17 | 0.002 | 0.986 | 0.195 | 0.93 | 0.884
Cardiologist# | 0.652 | 0.5 |  |  | 0.408 | 0.504 |  |  |  |  | 
* Se – sensitivity, Pr – precision, FPR – false positive rate, Acc – accuracy, Sp - specificity
# https://www.ncbi.nlm.nih.gov/pmc/articles/PMC6784839/
Even with extensive tuning ensemble machine learning models had low classification performance (below)

## Slide 12: Heartbeat classification works better with convolutional neural nets
Went back to the 360-dimensional dataset before PCA transformation
Trained and tuned convolutional neural nets of various architecture
  1-4 layers, 16-72 nodes, 3-6 kernel size, 0.2-0.5 dropout rate

## Slide 13: Refined model use case
Expedite and simplify cardiologist review process instead of replacing
Sample beat review workflow:
  The model predicts and labels the abnormal beats
  Cardiologist reviews all abnormal predictions
  With 24-48h recording sensitivity is not an issue
  Precision should be as high as possible to save time
Pick a model based on maximum time saving:
Time saving
86%
83%

## Slide 14: Best performing model architecture
Input layer
Dropout
Conv1D
Dropout
MaxPool
3x
Flatten
Dense
Output layer
High level architecture
All dropout rate 0.25
3 convolution layers each with:
  32 filters
  kernel size 5
  RELU activation
  1 maxpool layer
1 dense layer with:
  32 nodes
  RELU activation

## Slide 15: Model training and classification summary
Epochs
Loss
Model has high variance
Expected because of inter-record variation
Longer training did not improve F1 score
S class has poor sensitivity compared to V class
F class is nearly not detected
If all abnormal beats are reviewed 22% extra of the S class and 28% extra of the F class beats will be found

## Slide 16: The model has variable but adequate performance for general use
poor
adequate
good
Class V identified better than class S
Different records have varying sensitivity and recall for classes V and S
Class F poorly identified across records, probably because ~91% of class F beats belong to 2 records
Overall specificity and accuracy are high for all records because of heavy class imbalance

## Slide 17: Model output visualization
Labeled heartbeat records available on Heroku for easy navigation:
https://arrhytmia-detector.herokuapp.com